## Slide 1
“Calendar w/ Temperature & Binary Clock“
By: Doding

## Slide 2: Overview
  Requirements
  Requirement Key Points
  Hardware
  Software
    Software modules
    Software Framework
      State Machine (FSM)
    Event Handling
    Serial Console Event Handling
      Command Set
      Command Parsing
      UART Buffering
    Storage Module
      One way of storing information in physical memories.
    Application Tick
    Temperature Sensing
    Display Manager
    Calendar and Clock Module
    Button
  System Priorities
  Software – All Together
Notes: 1.) In requirement slides will discuss about
- one way of doing requirement capture is by using UML
- using UML to analyze use cases
- I will show you an actual UML models
- basically, will talk about what are the things I did before I start thinking about What Software modules I need and What Software Framework is best fit for the job.
2.) In Hardware will talk about its high level diagram.

## Slide 3: What you need:
  PIC24FJ128GA010 MCU PIM
    http://www.microchip.com/wwwproducts/en/PIC24FJ128GA010
  XC16 Compiler
    http://www.microchip.com/mplab/compilers
  PIC24/dsPIC Peripheral Libraries v2.00 – Windows
    http://www.microchip.com/mymicrochip/filehandler.aspx?ddocname=en574967
  Explorer 16 Board
  ICD-3
  MCP2200
  Serial Terminal such as Real Term

## Slide 4: Requirements
The Date, Day and Ambient Temperature will be displayed on the LCD.
The Time will be displayed using LEDs (Binary Clock). This will be on a 24-hour format.
  The LEDs will display the hour for 2.5 seconds. D8-D7 for the tens, D6 to D3 for the one. D10 is always ON to identify that it is hours.
  The LEDs will then display the minutes for 2.5 seconds. D9-D7 for the tens, D6 to D3 for the one. D10 is always OFF to identify that it is minutes.
RS232 Menus:
  Update Date
  Update Time
  Set Alarm
  Save Time/Date to Internal EEPROM
  Save Time/Date to External EEPROM
  View Time/Date from Internal EEPROM
  View Time/Date from External EEPROM
  Feel free to design the Sub Menus for the items on (3).
  The Internal EEPROM should be simulated (refer to Data EEPROM Emulation Application Note).
  The LEDs will blink (250mS ON/OFF) during an Alarm. A push button switch will cancel the Alarm and will return to the normal display of the Binary Clock.
  Let us target a 1sec +/- 100uS accuracy for the clock.
Notes: 1.) This slide is not the best as it has many information in it but we will take it slow to capture what we need here.

## Slide 5: Requirement Key Points
Events
  Human generated events such as serial console commands and button events.
  Human generated events are not super fast.
  Alarm Event generated by the RTCC.
    Fastest alarm event is every 0.5 seconds.
Human Interface
  No animation is required.
  Display info are in fixed positions.
  Serial Console.
  Buttons.
  LED for the binary clock
Buffering
  No data streaming.
  Fifo based buffer is enough.
  We have enough memory to avoid dynamic memory allocation.
The entire requirement have fixed number of states.
  Hierarchical State Machine is not needed.
  Single level state machine is enough to support all functionalities.
Notes: 1.) After requirement capture I normally write down some key points where I can based my design.

## Slide 6: Hardware
MCU
INT0
RTCC
TIMER
ADC
SPI
iEEPROM
UART
PMP
GPIO
LEDs
LCD
CONSOLE
xEEPROM
TEMP_SENSE
BUTTONS
Notes: 1.) 16bit MCU
2.) GPIO to control LED
3.) Parallel Master Port is used to control the LCD display
4.) UART to receive commands and show text into serial console.
5.) iEEPROM, this is an Emulated EEPROM
6.) SPI to write and read with an external EEPROM.
7.) ADC to monitor ambient temperature.
8.) 1 Timer is used as the application tick. But not used in clock and calendar.
9.) RTCC for calendar, binary clock and Alarm
10.) INT0 to detect button events.

## Slide 7: Software Framework
FIFO
State Machine
Engine
Event handler 1
LUT
External Events
event
Internal Events
Event handler 2
Event handler 3
Event handler 4
Event handler etc..
tick
sys_info
temp_sense
display
Notes: 1.) From left to right
2.) Event are 2 types:
- external events like button press, console commands.
- all external events are from ISR.
- internal events are for example Alarm and Internal Errors like while accessing eeprom, etc..
3.) All events are queued to make sure that nothing is missed.
- first in first out
4.) the state machine is running in infinite loop always checking if there is an item in the fifo.
- when the state machine detects an item in the queue it will query the LUT to determine which event handler to execute.
5.) the look up table will decide which handler to execute based on the FSM State and the Event.
6.) sys_info
- is a shared data structure containing:
- time
- date
- temperature
7.) the tick is a timer ISR running in background that keeps on updating LCD and LED based on sys_info

## Slide 8: Serial IO Buffering

## Slide 9: How does it all fit together?

## Slide 10: End
Thank You!!